## Slide 1
BUS 9430 · CAPSTONE 2 · DATA UNDERSTANDING AND PREPARATION
Tomorrow's Sun,
Today's Plan
What our data shows, and how we get it ready
Team Solar Foresight
Team: Carolina Lenes Arreola, Juan David Jaimes, Mohammad Mahmud, Vince Lanzillo and Raúl J. Solá Navarro
November 16, 2026
Notes: [RAUL, slides 1 to 3. Finish by 0:15] Good morning. We're Team Solar Foresight. Last time we told you the problem and the plan. Today is about the data: what we have, what it shows, and how we get it ready.

## Slide 2
THE BUSINESS PROBLEM
Solar is the part of tomorrow's plan that depends on the weather
WHAT CAISO DOES
Locks in tomorrow's plan today
Bids close at 10 a.m. Pacific. The plan is out by 1 p.m.
WHAT GOES WRONG
The solar forecast misses
Too high: backup power bought at the last minute. Too low: reserves held for nothing.
WHAT WE FORECAST
Hourly solar output, a day ahead
In megawatts (MW), using only what is known at 10 a.m. Not demand: CAISO already forecasts that.
Notes: [Finish by 0:55] CAISO runs California's main grid and locks in tomorrow's plan today: bids close at 10 a.m. and the plan is out by 1 p.m. [click] Solar depends on tomorrow's weather, so when the forecast misses, someone pays: backup power bought at the last minute, or reserves held for nothing. [click] We forecast one thing: hourly solar output a day ahead, in megawatts, using only what is known at 10 a.m. We do not forecast demand, because CAISO already does.

## Slide 3
THE DATA
Five public sources, one hourly table
ANSWER KEY
EIA
Actual solar output, hour by hour
INPUTS
Open-Meteo
Weather forecasts made before 10 a.m.
BENCHMARK
CAISO
Its own day-ahead solar forecast
SCALE
EIA Form 860M
Installed solar capacity
FLAGS
CAISO curtailment
Solar that was turned down
PERIOD
Mar 2024 to Oct 2026
954 days
HOURLY ROWS
22,896
11,733 in daylight
HOURS WITH A GAP
< 1%
225 hours, all documented
Privacy: low. Public, system-wide data, no personal information. Delivery: raw files saved in our repository; the weather service's free tier is non-commercial and capped per day.
Weather data by Open-Meteo.com (CC BY 4.0).
Notes: [Finish by 1:55] Our data comes from five public sources. EIA gives the answer key: actual solar output. Open-Meteo gives weather forecasts made before the 10 a.m. deadline. CAISO gives its own forecast, which is our benchmark. And two smaller files tell us how much solar is installed, and how much was turned down. [click] Together they make one table: 954 days and 22,896 hourly rows. Fewer than one hour in a hundred has a gap, and every gap is documented. [click] On privacy and delivery: privacy risk is low, because this is public, system-wide data with no personal information. The delivery risks are practical: the free weather service is non-commercial and capped per day, so we saved every raw file in our repository.

## Slide 4
WHAT THE DATA SHOWS
A regular daily shape, driven by season and weather
Average solar output (MW), by hour of the day, Pacific time
Chart: 
| 12 AM |  |  | 3 AM |  |  | 6 AM |  |  | 9 AM |  |  | Noon |  |  | 3 PM |  |  | 6 PM |  |  | 9 PM |  |
Winter | 0 | 0 | 0 | 0 | 0 | 15 | 1507 | 5720 | 9834 | 11449 | 11841 | 11878 | 11790 | 11243 | 9348 | 5190 | 1339 | 54 | 0 | 0 | 0 | 0 | 0 | 0
Spring | 0 | 0 | 0 | 0 | 0 | 482 | 3260 | 8531 | 12382 | 13667 | 14092 | 14288 | 14172 | 13879 | 13332 | 12612 | 11250 | 7945 | 2937 | 276 | 1 | 0 | 0 | 0
Summer | 0 | 0 | 0 | 0 | 0 | 827 | 4743 | 10940 | 14829 | 16403 | 17141 | 17414 | 17448 | 17188 | 16677 | 15991 | 14702 | 11450 | 5512 | 949 | 0 | 0 | 0 | 0
Fall | 0 | 0 | 0 | 0 | 0 | 0 | 1111 | 5851 | 11780 | 14129 | 14768 | 14912 | 14798 | 14492 | 13852 | 12136 | 8463 | 3596 | 488 | 0 | 0 | 0 | 0 | 0
+47%
Summer midday peak versus winter.
68% vs 41%
Midday output on clear versus very cloudy forecast days, as a share of capacity.
+24%
Installed solar since March 2024, and up to 1 in 4 possible MWh turned down in spring.
Average solar output by hour, March 2024 to April 2026, Pacific time. Sources: EIA, Open-Meteo, CAISO.
Notes: [CAROLINA. Finish by 3:10] Here is what the data shows. [click] Solar follows a very regular daily shape: up at 6, peak at noon, done by 8. Summer's midday peak is about 47 percent higher than winter's. [click] Weather matters: on clear days solar delivers about 68 percent of installed capacity at midday, on very cloudy days about 41 percent. [click] And two things change over time. Installed solar grew 24 percent, so we scale every error by capacity. And in spring, up to one in four possible megawatt-hours is turned down, so we flag those hours.

## Slide 5
GETTING IT READY
From raw data to a fair test
1
One clock
Every source on the same hour.
2
Fix gaps
Fill short ones, drop long ones.
3
Flag turned-down solar
Report with and without.
4
Scale by capacity
So months compare fairly.
Mar 2024
Oct 2026
All the days
Training days (earliest 80%, 763 days)
Test (191 days)
Locked until the end
The test is the latest 191 days (April 10 to October 17, 2026). It stays locked until the end and has no winter, so we judge winter in validation.
Notes: [JUAN DAVID. Finish by 4:20] Now, how we get the data ready. Four steps. [click] Put every source on one clock. [click] Fix gaps: fill short ones, drop long ones. [click] Flag the hours when solar was turned down and report results with and without them. [click] Scale errors by installed capacity so a month in 2024 compares fairly with a month in 2026. [click] Then we split the days in time order. The models learn from the earliest 80 percent. The latest 191 days stay locked until the end. One honest limit: that block has no winter, so we judge winter in the validation checks.

## Slide 6
THE BAR TO BEAT
Our scorecard starts with CAISO
SAME AS YESTERDAY
4.9%
Average miss, as a share of capacity. The floor to beat.
CAISO, AS PUBLISHED
5.7%
About 830 MW too high on average.
CAISO, ADJUSTED
3.7%
With turned-down solar added back. The fairest picture of CAISO's skill.
OUR TARGET: NO MORE THAN 1.25 TIMES CAISO'S MISS
4.6% to about 7%, depending on which CAISO number counts
WATCHING Short history, no winter in the test, weather timing at 10 a.m.
NEXT Compare models Nov 17 to Dec 8. Results Dec 14.
Notes: [JUAN DAVID. Finish by 5:30] Last, the bar to beat. We scored the reference forecasts on our own data. [click] Same as yesterday misses by 4.9 percent of installed capacity. CAISO's published forecast misses by 5.7 percent, because it runs about 830 megawatts too high. Add back the solar that was turned down and CAISO's miss is 3.7 percent. [click] Our target is no more than 1.25 times CAISO's miss, which is 4.6 to about 7 percent depending on which number counts. We will fix that before modeling and report both. [click] Our watch list is short history, no winter in the test, and weather timing. Next we compare models, with results on December 14. We would welcome your view on anything we should check before we build them. Thank you.