## Slide 1
BUS 9430 · CAPSTONE 2 · DATA UNDERSTANDING AND PREPARATION
Tomorrow's Sun,
Today's Plan
What our data shows, and how we get it ready
Team Solar Foresight
Team: Carolina Lenes Arreola, Juan David Jaimes, Mohammad Mahmud, Vince Lanzillo and Raúl J. Solá Navarro
November 16, 2026
Notes: [RAUL, slides 1 to 5] Good morning. Last time we told you the problem and the plan. Today we show the data: what we collected, what we found in it, and how we are getting it ready for modeling. We start with a short reminder of the problem, because everything else depends on it.

## Slide 2
THE BUSINESS PROBLEM
Solar is the part of tomorrow's plan that depends on the weather
WHAT CAISO DOES
Locks in tomorrow's power plan today
Bids close at 10 a.m. Pacific. The plan is published at about 1 p.m. It says which plants run tomorrow and how much each makes.
WHAT GOES WRONG
The solar forecast misses
Too high, and operators buy backup power at the last minute. Too low, and they hold reserves they never use.
WHAT WE DO
Forecast solar output a day ahead
Hour by hour, using only what is known at 10 a.m. We then compare ourselves with CAISO's own forecast.
Notes: CAISO runs California's main power grid. It locks in tomorrow's plan today: bids close at 10 a.m. Pacific and the plan comes out around 1 p.m. Solar is a big part of that plan, and it depends on tomorrow's weather. When the solar forecast is wrong, somebody pays: either backup power bought at the last minute, or reserves held for nothing. Our project is a better day-ahead solar forecast.

## Slide 3
WHAT WE FORECAST
We forecast solar output, not electricity demand
TOTAL DEMAND
What customers use
−
WIND AND SOLAR
What the weather supplies
=
NET LOAD
What gas, batteries and imports must cover
DEMAND
CAISO already forecasts it
It is a different problem, and the operator has its own tools for it.
OUR TARGET VARIABLE
Hourly solar output, in megawatts (MW)
How much power utility-scale solar plants in the CAISO area actually produce each hour, as measured by the U.S. Energy Information Administration.
Net load definition: U.S. Energy Information Administration (EIA).
Notes: A fair question last time was why we are not forecasting energy use. Demand matters, but CAISO already forecasts it. What the grid operator plans around is net load: demand minus what wind and solar supply. Solar is the weather-driven part of that equation, so a better solar forecast changes how much gas, battery or import power has to be lined up. Our target variable is the hourly output of utility-scale solar in the CAISO area, in megawatts, as measured by the EIA.

## Slide 4
THE DATA
Five public sources, one hourly table
ROLE | SOURCE | WHAT IT GIVES US | WHAT WE PULLED
Answer key | EIA Hourly Electric Grid Monitor | Actual hourly solar output for the CAISO area | Hourly, Jan 2024 to Oct 17, 2026
Inputs | Open-Meteo Previous Runs | Weather forecasts published before the 10 a.m. bid close | 51 locations across California, Mar 2024 to Oct 2026
Benchmark | CAISO OASIS, report SLD_REN_FCST | CAISO's own day-ahead solar forecast | Hourly, same dates, three solar regions added up
Scale | EIA Form 860M | Installed solar capacity, so errors compare fairly over time | Monthly, Mar 2024 to Sep 2026
Flags | CAISO curtailment files | Solar that was turned down because the grid could not use it | Mar 2024 to Oct 2026
Weather data by Open-Meteo.com (CC BY 4.0). All data files are saved in the team repository.
Notes: These are the five sources, and all of them are public. The EIA series is the answer key. Open-Meteo provides the weather forecasts we use as inputs. CAISO's own forecast is the benchmark and is never used for training. EIA Form 860M gives installed capacity so we can compare errors fairly over time, and the curtailment files tell us which hours were turned down. Everything is saved in our shared repository, so any number in this deck can be reproduced.

## Slide 5
THE RULE THAT KEEPS THE TEST HONEST
We may only use what is known at 10 a.m.
ALLOWED (MAIN MODEL)
Weather forecast made two days before
Published before the 10 a.m. bid close for every hour of the next day. This is the input we use.
COMPARISON ONLY
Weather forecast made one day before
For afternoon hours it is likely published after the bid close. We run it only as a labeled comparison, never as our result.
Why it matters: a forecast that peeks at later information looks better than it could be in real life.
Both versions are in the data, so the comparison is a single switch.
Notes: CAISO closes bids at 10 a.m. Pacific the day before. Any input we use has to be available by then. Weather models publish a few hours after they start running, so a forecast made one day before the target hour may arrive after the deadline for afternoon hours. Our main model therefore uses the forecast made two days before, and the one-day-before version is shown only as a clearly labeled comparison. [Hand off] Carolina will show you what the data looks like.

## Slide 6
DATA UNDERSTANDING
The data at a glance: nearly complete
PERIOD COVERED
Mar 2024 to Oct 2026
954 days, from March 8, 2024 to October 17, 2026.
HOURS OF DATA
22,896
One row per hour. 11,733 of them are daylight hours, when solar can make power.
HOURS WITH A GAP
< 1%
225 hours across all sources, out of 22,896. Gaps are in the weather feed (129), the CAISO forecast (72) and EIA (24).
So the data is in good shape before we change anything.
Notes: [CAROLINA, slides 6 to 12] Thank you, Raul. Here is the data at a glance. We cover 954 days, from March 8, 2024 to October 17, 2026. That is 22,896 hourly rows, and 11,733 of them are daylight hours, when solar can make power. Fewer than one hour in a hundred has a gap in any source: 129 in the weather feed, 72 in CAISO's forecast and 24 in the EIA series. So the data is in good shape before we do anything to it.

## Slide 7
DATA UNDERSTANDING
A typical solar day: up at 6, peak at noon, done by 8
Average solar output (MW), by hour of the day, Pacific time
Chart: 
| 12 AM |  |  | 3 AM |  |  | 6 AM |  |  | 9 AM |  |  | Noon |  |  | 3 PM |  |  | 6 PM |  |  | 9 PM |  |
Winter | 0 | 0 | 0 | 0 | 0 | 15 | 1507 | 5720 | 9834 | 11449 | 11841 | 11878 | 11790 | 11243 | 9348 | 5190 | 1339 | 54 | 0 | 0 | 0 | 0 | 0 | 0
Spring | 0 | 0 | 0 | 0 | 0 | 482 | 3260 | 8531 | 12382 | 13667 | 14092 | 14288 | 14172 | 13879 | 13332 | 12612 | 11250 | 7945 | 2937 | 276 | 1 | 0 | 0 | 0
Summer | 0 | 0 | 0 | 0 | 0 | 827 | 4743 | 10940 | 14829 | 16403 | 17141 | 17414 | 17448 | 17188 | 16677 | 15991 | 14702 | 11450 | 5512 | 949 | 0 | 0 | 0 | 0
Fall | 0 | 0 | 0 | 0 | 0 | 0 | 1111 | 5851 | 11780 | 14129 | 14768 | 14912 | 14798 | 14492 | 13852 | 12136 | 8463 | 3596 | 488 | 0 | 0 | 0 | 0 | 0
WHAT WE SEE
Summer peaks about 47% higher than winter
About 17,400 MW at midday in summer, versus 11,900 MW in winter.
WHAT IT MEANS FOR THE MODEL
Hour of day and season matter
The model has to know both, so we give them to it directly.
Average over March 2024 to April 2026. Winter is December to February. Source: EIA.
Notes: This is the average solar day, by season. Output starts around 6 a.m., peaks at midday and is finished by about 8 p.m. in every season. In summer the midday peak averages about 17,400 megawatts. In winter it is about 11,900, roughly a third lower. The shape is very regular, which is good news. The hard part is not the shape, it is how much of that shape the weather gives us on a particular day. For the model, that means hour of day and season have to be inputs.

## Slide 8
DATA UNDERSTANDING
Cloudier forecast, less solar
Midday output, % of installed solar capacity, by forecast cloud cover
Chart: 
| Clear (0 to 10%) | Some cloud (10 to 30%) | Cloudy (30 to 60%) | Very cloudy (60 to 100%)
Midday output, % of capacity | 67.6 | 57.4 | 51.6 | 41.4
0.87
How closely forecast sunshine tracks actual output, where 1.0 is perfect. Measured across 9,188 daylight hours.
55%
Biggest one-day drop: on October 10, 2026, output fell from 161 to 73 gigawatt-hours (GWh) in a day.
Midday = 11 a.m. to 2 p.m. Pacific. Cloud cover is the forecast made two days earlier. All seasons, so winter's lower sun also plays a part. Sources: EIA, Open-Meteo.
Notes: Here is why weather is worth forecasting. We grouped midday hours by how cloudy the forecast said it would be. On clear days, solar delivers about 68 percent of installed capacity at midday. On very cloudy days it is about 41 percent. Part of that gap is winter sun, which is lower, but the link is strong. Across more than nine thousand daylight hours, the forecast sunshine and the actual output move together with a correlation of 0.87. And the weather can change fast: on October 10 of this year, output fell by 55 percent from one day to the next. That is the kind of day that costs a grid operator money.

## Slide 9
DATA UNDERSTANDING
More panels every month, and more solar turned down
Installed solar capacity grew 24% (GW)
Spring is when solar gets turned down (% of possible)
Chart: 
| Mar 2024 |  |  |  |  |  |  |  |  |  | Jan 2025 |  |  |  |  |  |  |  |  |  |  |  | Jan 2026 |  |  |  |  |  |  |  | Sep 2026
Installed solar capacity (GW) | 20.98 | 20.99 | 21.12 | 21.33 | 21.49 | 21.51 | 21.53 | 21.6 | 21.8 | 22.79 | 23.02 | 23.48 | 23.36 | 23.62 | 23.73 | 23.63 | 23.8 | 24.16 | 24.17 | 24.18 | 24.35 | 24.85 | 24.87 | 24.94 | 24.95 | 24.96 | 25.14 | 25.16 | 25.81 | 25.81 | 26.03
Chart: 
| Mar 2024 |  |  |  |  |  |  |  |  |  | Jan 2025 |  |  |  |  |  |  |  |  |  |  |  | Jan 2026 |  |  |  |  |  |  |  | Sep 2026 |
Solar turned down (%) | 17.6 | 16.8 | 11.6 | 4.1 | 1.2 | 1.4 | 2.6 | 3.7 | 5 | 0.7 | 3.8 | 14.7 | 20.1 | 13.3 | 6.6 | 4.2 | 2.3 | 2.3 | 3.6 | 5.4 | 0.9 | 1.1 | 0.8 | 7.1 | 14.3 | 24.2 | 21 | 8.6 | 3.6 | 2.5 | 3.2 | 4.3
WHY IT MATTERS
Errors must be scaled by capacity
From 21.0 to 26.0 GW. A 1,000 MW miss meant more in 2024 than it will in 2026, so we report errors as a share of capacity.
WHY IT MATTERS
Turned-down solar hides true output
In April 2026 about 1 in 4 possible megawatt-hours was turned down (24%). Over the whole period it is 7.6%.
Sources: EIA Form 860M (capacity, includes about 2.8 GW in Arizona and Nevada); CAISO curtailment reports.
Notes: Two patterns the model has to live with. On the left, installed solar capacity grew from about 21.0 to 26.0 gigawatts, a 24 percent increase in under three years. So we cannot compare raw megawatt errors across years; we express every error as a share of installed capacity. On the right, curtailment. This is solar that plants could have produced but the grid turned down, usually in spring when it is sunny and demand is low. In April 2026 about one in four possible megawatt-hours was turned down. Across the whole period it is 7.6 percent. Because the measured output is lower on those days, we flag those hours and report results with and without them.

## Slide 10
DATA UNDERSTANDING
Four data problems, and what we do about each
ISSUE | WHAT WE FOUND | WHAT WE DO
Clocks disagree | EIA reports in UTC. CAISO files use the local clock, which shifts with daylight saving time. | Convert every source to one clock (hour ending, UTC) and check against sunrise and sunset.
Missing hours | 225 of 22,896 hours (under 1%): weather 129, CAISO forecast 72, EIA 24. | Fill short gaps, drop long ones, and say which.
Turned-down solar | 7.6% of possible solar energy over the period. Up to 24% in a spring month. | Flag those hours and report results with and without them.
More panels over time | Installed capacity up 24%, from 21.0 to 26.0 GW. | Scale errors by installed capacity so months compare fairly.
Also noted: tiny negative readings at night (about 40 MW below zero, against peaks of 17,000 MW). They are handled explicitly.
Notes: These are the four data problems we found, and each one has a written rule. Clocks: EIA is in UTC and CAISO files follow the local clock, so we convert everything to one clock and check it against sunrise and sunset. Missing hours: fewer than one percent, mostly in the weather feed. Turned-down solar: we flag it. More panels over time: we scale errors by installed capacity. One more small thing: at night the EIA series shows tiny negative values, about 40 megawatts, which is negligible next to 17,000 at midday but we treat explicitly.

## Slide 11
PRIVACY AND DELIVERY RISKS
Low privacy risk, three delivery risks
PRIVACY: LOW
Public, system-wide data
No customers, households or personal information. The capacity file names power plants and companies, which are public records.
Open-Meteo requires credit (CC BY 4.0) and its free tier is non-commercial. EIA and CAISO data are public, and we cite them.
DELIVERY RISK 1
Timing at 10 a.m.
A forecast is only useful if its inputs exist by the bid close. A late weather feed would break it.
We use the two-day-ahead forecast and check the one-day version only as a comparison.
DELIVERY RISK 2 AND 3
Limits and reproducibility
The free weather service caps daily calls. Our full pull used about 6,500 of the 10,000 allowed in a day.
Raw files are saved in the repository with a data dictionary, so nobody needs to re-pull.
Notes: The syllabus asks us to assess privacy and delivery risks as well as data quality. Privacy risk is low. All five sources are public and system-wide: no customers, no households, no personal information. The capacity file names power plants and companies, but those are public records. The licensing points are to credit Open-Meteo and to remember that its free tier is non-commercial. Delivery has three risks. First, timing: the inputs must exist by 10 a.m. Second, limits: the free weather service caps daily calls, and our full pull used about 6,500 of the 10,000 allowed in a day. Third, reproducibility: we saved the raw files and a data dictionary in the repository so the team never has to re-pull.

## Slide 12
THE BAR TO BEAT
How good is CAISO's own forecast on our data?
SAME AS YESTERDAY
4.9%
Average miss as a share of installed capacity. The floor to beat. It is 6.1% if limited to what is known at 10 a.m.
CAISO, AS PUBLISHED
5.7%
Runs about 830 MW too high on average, because it plans for solar that is then turned down.
CAISO, ADJUSTED
3.7%
With turned-down solar added back. The fairest picture of CAISO's skill. The gap to actual output almost disappears.
OUR TARGET: NO MORE THAN 1.25 TIMES CAISO'S MISS
That means 4.6% to about 7%, depending on which CAISO number counts
We will fix this before modeling and show both numbers.
Scored on 9,144 daylight hours in the training and validation days (March 2024 to April 9, 2026). The test days stay locked.
Notes: Before building any model we score the reference forecasts on our own data. Same-as-yesterday misses by 4.9 percent of installed capacity. CAISO's published day-ahead forecast misses by 5.7 percent, and it runs about 830 megawatts too high on average. Most of that bias disappears when we add back the solar that was turned down, and then CAISO's miss is 3.7 percent. Part of that is by construction, because CAISO defines curtailment against its own forecast, so we show both. Our target was to be within 1.25 times CAISO's miss. That is 4.6 percent or about 7 percent depending on which number counts. We will settle that before modeling and report both. One more detail: same-as-yesterday uses afternoon information that is not available at 10 a.m., and if we limit it to what is known then, it is 6.1 percent. [Hand off] Juan David will take you through how we prepare the data.

## Slide 13
DATA PREPARATION
From five sources to one table
1
Pull
Download each source for the same dates.
2
Align
One clock, one row per hour.
3
Clean
Handle gaps and flag curtailed hours.
4
Add features
Hour, season, sun angle, scaled by capacity.
5
Split
Time-ordered training, validation and test sets.
Steps 1 and 2 are done: 22,896 aligned hourly rows. Steps 3 to 5 follow the rules on the previous slides.
Notes: [JUAN DAVID, slides 13 to 17] Thank you, Carolina. Five steps. Pull the sources for the same dates. Align them on one clock with one row per hour. Clean gaps and flag curtailed hours. Add features such as hour of day, season and sun angle. Then split the table in time order so the models are always tested on days they have not seen. Steps one and two are done: we have a merged table of 22,896 aligned hourly rows.

## Slide 14
DATA PREPARATION
Test on days the model has never seen
Mar 2024
Oct 2026
All the days
Training days (earliest 80%, 763 days)
Test (191 days)
Locked until the end
FOUR ROLLING CHECKS ON THE TRAINING DAYS, USED TO TUNE SETTINGS
Check 1
Train
Validate
untouched
Check 2
Train
Validate
untouched
Check 3
Train
Validate
untouched
Check 4
Train
Validate
untouched
1
Train
The earliest 80% of days (763 days, to April 9, 2026) teach the models.
2
Validate
Four rolling checks of about three months each compare the models and tune them.
3
Test
The latest 191 days (April 10 to October 17, 2026), scored once at the end. No winter, so winter is judged in validation.
Notes: We split in time order, never at random, because a forecast is always about the future. The earliest 80 percent of days, 763 of them, is for training and for four rolling checks. The latest 191 days, April 10 to October 17 of this year, is locked until the end and scored once. One honest limit: that last block runs from spring to mid-October, so it has no winter, and we judge winter accuracy in the validation checks instead.

## Slide 15
WHAT COMES NEXT
We choose models after we see the data
STEP 1
Score the two reference forecasts
→
STEP 2
Explore the data
→
STEP 3
Shortlist candidate models
→
STEP 4
Compare on the same folds
JUDGED ON
Average miss compared with CAISO
JUDGED ON
Worst-case overshoot, which drives backup power
JUDGED ON
How easily we can explain it
Step 1 is done: see the bar to beat.
Notes: We have deliberately not picked our models yet. The first step, scoring the reference forecasts, is done. Next we explore the data and shortlist candidates, then compare them on the same time-ordered folds. The winner is chosen on three things: average miss compared with CAISO, worst-case overshoot, because that is what drives backup power, and how easily we can explain it.

## Slide 16
RISKS AND OPEN DECISIONS
Four things we are watching
SHORT HISTORY, NO WINTER IN THE TEST
About two and three-quarter years
Each calendar month appears two to three times. The test block runs April to October, so we judge winter in validation and say so plainly.
WHICH YARDSTICK
CAISO's number depends on turned-down solar
Its miss is 5.7% as published and 3.7% with turned-down solar added back. We report both and fix the target before modeling.
WEATHER TIMING
Which forecast is available at 10 a.m.
Main model uses the forecast made two days before. The one-day version is a labeled comparison.
TURNED-DOWN SOLAR
Concentrated in spring, inside our test block
April and May 2026 saw 21% to 24% turned down. We flag those hours and report results with and without them.
Notes: Four risks. History is short, so each month appears only two to three times, and the test block has no winter. CAISO's number depends on how you treat turned-down solar, so we report both and fix our target before modeling. The weather timing rule is confirmed in the data and we keep the one-day version only as a comparison. And turned-down solar is concentrated in spring, which is inside our test block, so those hours are flagged and results are reported with and without them.

## Slide 17
NEXT STEPS
From a clean table to results
Nov 17–27
Explore the data and compare candidate models.
Nov 30–Dec 8
Score the models against CAISO and build the charts.
Dec 14
Capstone 3: models and results.
Your input: Is there anything in the data or the test design you would want us to check before we build models?
Notes: The next two weeks are exploration and model comparison. Then scoring and charts, and Capstone 3 on December 14. Before we start modeling, we would value your view on anything in the data or the test design we should check.

## Slide 18
APPENDIX A
Data dictionary: the main columns
COLUMN | MEANING | UNIT | SOURCE
hour_end_utc | The hour ending at this time, UTC (the key for joining all sources) | timestamp | All, aligned
eia_mw | Actual utility-scale solar output (target variable) | MW | EIA
caiso_dam_mw | CAISO day-ahead solar forecast (benchmark only) | MW | CAISO OASIS
capacity_mw | Installed solar capacity in that month | MW | EIA Form 860M
cloud_cover, shortwave_radiation, temperature_2m, ... | Weather forecast inputs, two-day-ahead version, capacity-weighted across locations | %, W/m², °C | Open-Meteo
curt_mwh | Solar energy turned down in that hour | MWh | CAISO curtailment files
Full list of columns, units and checks: docs/DATA_DICTIONARY.md in the team repository.

## Slide 19
APPENDIX B
Sources
U.S. EIA, Hourly Electric Grid Monitor and API; net load definition: eia.gov/opendata
U.S. EIA, Form 860M, monthly installed capacity: eia.gov/electricity/data/eia860m
Open-Meteo, Previous Runs API, CC BY 4.0: open-meteo.com/en/docs/previous-runs-api
CAISO, day-ahead market (bids close 10 a.m. Pacific, results about 1 p.m.): caiso.com/market-operations/products-services
CAISO OASIS, day-ahead solar forecast, report SLD_REN_FCST: oasis.caiso.com
CAISO, production and curtailments data (curtailment workbooks and daily renewables report): caiso.com/library/production-curtailments-data
Team repository, raw data, data dictionary, FAQ and how-to: github.com/RaulSolaNavarro/caiso-solar-forecast